## Slide 1: Solar tracker
Gattaux Gabriel
Andrei George Claudiu

## Slide 2: Summary
Introduction
Architecture
Electronics parts
Motorization
Algortihm
Improvements and Conclusion
Focus on electronics and motorization
Lake of printing

## Slide 3: Introduction
Additive manufacturing project :
  Goal : To construct a prototype of heliostat in plastic and ceramic
  Specifications :
  Rotational movement around vertical axis at least 270 degs
  Rotational movement around horizontal axis at least 90 degs
  Restricted volumic area of 120mm diameter and 150mm height
  Restricted width of the mirror, between 5mm and 12mm
Drive system project:
  Goal : To motorize our prototype of heliostat  solar panel tracker
  Specifications :
  Add a motorization system
  Bonus : Add sensors

## Slide 4: Overall Architecture
Global system
Azimuth’s joint with coupler
Altitude’s joint
Upper part – 2 in 1

## Slide 5: Electronics
Arduino UNO
Motor Shield L298D
Light Intensity Acquisition:
  LDR x3
Initial Condition Control:
  LED x1
  Buttom x1
  10k Pull-down Resistor
Elevation Control:
  Servo motor Hitec HS-55 x1
Azimuth Control:
  Stepper motor 17HS15
Power Supply:
  Battery 9V
  Power supply 12[V] 1 [A]
Electric Circuit
Initial Condition
Notes: Remember to explain all the technical stuff (how we did initial condition and why, ecc ecc), powe supply

## Slide 6: Motorisation
Stepper motor  Azimuth’s joint
Controlled using single step and double coil
Through L298D  The driver do the all calculation
Library Arduino : AF_stepper
Vitesse : 10 rpm (more couple, less speed)
Servo motor  Altitude’s joint
Through L298D
Library Arduino : stepper
Pros / Cons
Pros / Cons
Direct angle input
Less power supply
Good at prototyping
Noise
Less precise position
180 deg of range
Step input
Big power consumption
Very precise position
No noise
360 deg

## Slide 7: IDE Steps
Initialization of the variables
Initial configuration mode
Data acquisition from LDRs and motors
Computational Algorithm
Motors Control

## Slide 8: Improvements
Direct Matlab Control
Others
Algorithm implemented on Stateflow
Refreshing period by adapting the refreshing rate of the control loop depending of the light intensity
Trajectory optimization by controlling the motion of each axis one at time
3. Power supply optimization by displacing in a better way the servo motor or using the energy produced by the solar panel itself
4. Wiring optimization by wires fixing and introducing also a fixed base
ULN2003

## Slide 9: Conclusion
This project  Affected by the Additive manufacturing project (CAD, print…)
Good to create a project from 0
Using 2 servo instead of 1 stepper to have a “pick and place” system
Project succeed  Specification filled / Time-schedule OK
SKILLS GAINED :
3D printing
Electronics programming
Drive system
Project management

## Slide 10: Thanks you feel free to ask questions (French or English :)